Wireless WIFI Intraoral Camera JVE-K013

①LED light  ②Camera  ③photo/video Indicator   ④Brightness indicator  ⑤On/Off indicator  ⑥Photo/Video ⑦Brightness key  ⑧On/Off  ⑨Power indicator  ⑩USB port

Details

Pixels：5Mega               
Light resource：6pcs white LED light （5600K）

Dimming：Five brightness adjustment
Focus range：10mm--50mm
Photography Angle：105°                                                          
Connection：WIFI

End-User：1 users at the same time

Distance: ≥30m（open space）

D.C：3.7V

Battery capacity: 1000mA/h

Working time：180mins

Charging time: 2 hours

Application

1Two-way take photo and video simultaneously.

2.720P HD

- Transfer image by WIFI

- Real-time watching, oral examination

Operation

Please scan QR code as Photo-1 or search JVE in Apple Store/Android market/Google Play Store and install the app into your smart device first

1.Press ON/Off button 3 seconds to act the device, then the power and photo indicator will   keep on.

2. Open the WIFI Setting in your smart phone or Tablet PC and connect to WIFI Called JVE ,password is 12345678. You will see the image as following image as photo-2 in the APP after connected WIFI successfully.

Photo-1(IOS&Android&Google)            Photo-2

Details:①Light up ②Light down ③Folder ④Setting ⑤Battery ⑥Flip ⑦Front camera ⑧Video ⑨Photo

3.LED+/- Button can adjust the brightness of the light.

4.Press the brightness key to adjust brightness of the led light

5.Photo/Video Button : Press it shortly into photo mode, the blue light will flash 1 time. Press it longer into video mode, the indicator will keep flash, then press it again. The photo or video will be saved automatically.

Indicators

Low Battery: Red light will keep flashing；

Charging: Red light keep on；please disclose the cover at the bottom of the device and charge it through the USB port.

Full charged: Indicator light Off, but the on/off indicator will keep on；Charge 1 more hour after full-charged.

Working : Green light On；

Connect with Smart phone or PC: Green light keep flashing；

Photo: Indicator will flash 1 time

Recording: Indicator keep flashing

Faults and Solutions

1.No image on APP,  Solution: Please check if the WIFI connected correctly or not, and make sure if there only has 1 end-users connected at the same time. If yes, please restart the device. Please delete the WIFI Key APP before using the APP.

2.Stuck image or snow image, solution: Please check if the battery is full charged or not , if yes, Please restart the device.

3.Please scan the QR code with browser if you can not download APP through wechat.