Wireless WIFI Ear Camera JVE-K03F

① Camera ② Power Indicator ③Signal Indicator ④On/Off/Function key ⑤ Video/Photo ⑥ Charge port

Details

Pixels：5Mega               
Lens diameter:5.5mm

Sensor size:1/5 inch

Signal distance: 3M

View Angle:70 degree
Focus length: 2cm
Photography Angle：70°                                                          
Connection：WIFI

Image format: JPEG

Video format:AVI

Support system:Android/IOS

End-User：1 users at the same time

D.C：5V

Battery capacity: 500mA/h

Working time：180mins

Charging time: 2 hours

Application

1Two-way take photo and video simultaneously.

2.720P HD

- Transfer image by WIFI

- Real-time watching, oral examination

Operation

Please scan QR code and install the app into your smart device first

Android                    IOS

1.Press ON/Off button 3 seconds to act the device, then the power and photo indicator will   keep on.

2. Open the WIFI Setting in your smart phone or Tablet PC and connect with WIFI Look .. You will see the image in the APP after connected WIFI successfully.

- Press Power Button to adjust the brightness of the light.

4.Photo/Video Button : Press it shortly into photo mode, the blue light will flash 1 time. Press it longer into video mode, the indicator will keep flash, then press it again. The photo or video will be saved automatically.

Indicators

Low Battery: Red light will keep flashing；

Charging: Red light keep on；

Full charged: Indicator light Off, but the on/off indicator will keep on；Charge 1 more hour after full-charged.

Working : Green light On；

Connect with Smart phone or PC: Green light keep flashing；

Photo: Indicator will flash 1 time

Recording: Indicator keep flashing

Faults and Solutions

1.No image on APP,  Solution: Please check if the WIFI connected correctly or not, and make sure if there only has 1 end-users connected at the same time. If yes, please restart the device.

2.Stuck image or snow image, solution: Please check if the battery is full charged or not , if yes, Please restart the device.

Packing list :

1x WIFI Camera

1x charging cable

1x User manual

1x Mobile phone holder